## Slide 1
Comparison of off-line and on-line trained Gaussian process (GP) models for island groundwater management
Weijiang Yu
University of Sheffield, UK

## Slide 2
Island groundwater management problem
Management objective:
Minimize the operation cost of using island groundwater ()
Subject to:
Pct freshwater volume decrease =
Pumping intensity Q
Horrible computational cost
Simulation-optimization system
L = 1000 m
(RCH)
Numerous SEAWAT runs

## Slide 3
Framework of solving management problem by off-line and on-line trained GPs
Initial training sample
Develop GPs for objective function and constraints
Off-line training route
Identify new training points based on GP
Tolerance
Run full-scale model
Optimization solver
Optimal solution (WL, D)
Tolerance
Optimization solver
Optimal solution (WL, D) as new training point
Run full-scale model
Optimal solution (WL, D)
On-line training route
Run full-scale model
Update training points
Update training points

## Slide 4
Off-line training framework = 0.1RCHL, = 15%
Initial sample size = 4
LHS | Optimal Pumping (WL, D) | () | (%)
 | ( 260 m, 4 m) | 0.003574 | 13.23
 | ( 300 m, 5 m) | 0.003491 | 13.82
 | ( 270 m, 4 m) | 0.003560 | 13.68
LHS | Optimal Pumping (WL, D) |  | 
 | ( 260 m, 4 m) | 0.003574 | 13.23
 | ( 300 m, 5 m) | 0.003491 | 13.82
 | ( 270 m, 4 m) | 0.003560 | 13.68

## Slide 5
On-line training framework = 0.1RCHL, = 15%
Initial sample size = 4
LHS | Optimal Pumping (WL, D) | () | (%)
 | ( 50 m, 1 m) | 0.035432 | 1.81
 | ( 410 m, 10 m) | 0.064358 | 14.67
 | ( 280 m, 1 m) | 0.003558 | 13.90
LHS | Optimal Pumping (WL, D) |  | 
 | ( 50 m, 1 m) | 0.035432 | 1.81
 | ( 410 m, 10 m) | 0.064358 | 14.67
 | ( 280 m, 1 m) | 0.003558 | 13.90

## Slide 6
Conclusions
In the off-line training framework, optimal solutions from all LHS cases are close and reliable.
On-line training framework search for the optimal solution at a cheaper cost compared with the off-line training, but the results are less reliable. To get a reliable solution, initial samples should from the case of LHS() when using on-line training system.